CHICA top level description

# Current workflow
DESCRIPTION:
1. Calculates optimal arrangement and sections for the pipes inside each heat sink
2. Simulates one pipe for a given q(s), inlet conditions (T0,P0,etc), and
ASSUMPTIONS:
1. All plates are equal
2. All pipes with same heat flux density function, q(s)
3. All pipes for each bank have equal cross-section
4. All pipes have same length
5. One simulated pipe represents all the pipes within its bank
6. All simulation is steady-state (i.e. coolant has gone through a constant distribution along the pipe)

INPUTS
1. Input files:
  1. Heat flux density poloidal distribution to heat sink, q(s)
  2. Heat sink 2D cross section (x-z)
2. Machine parameters:
  1. Input number of plates
  2. Number of pipes (initial design value which may change with optimization)
  3. Input power density at divertor surface (assumes axis-symmetric for all plates)
3. Define cooling properties:
  1. Parameters for sensitivity analysis:
    1. Mass flow
    2. Channel velocity
  2. Fixed parameters:
    1. Input temperature
    2. Input pressure...
4. Channel geometry:
  1. Type
  2. Minimum material:
    1. from Plasma-facing surface to channels
    2. Between channels (minimum required, may be larger)
  3. Aspect ratio

CALCULATED (Shared) PARAMETERS:
1. input_rho – initial density
2. Plate geometry (to create or move):
  1. Number
  2. Angle of the panel. It will be used for initializing:
    thetap = 2*pi/n - (1*pi/180) # angle of the panel

OUTPUTS:
1. Channel geometry for Freecad:
  1. → coolant_geometry.asc – section of one pipe
  2. n → number of pipes per panel
  3. m→ number of rows in a panel
  4. nmin → minimum material thickness
  5. thetap → angle of the pipe array within the panel
2. Coolant results:
  1. Temperature profile T(s)
  2. HTC
  3. etc.

BLOCKS:
1. chica.py – Main procedure
  1. setup.initial_setup(…) – Populates lists and arrays needed for optimizing plate cooling pipes
    1. coolant_geometry.discrete_pipes_poloidal_flow(…) – Dimensioning of channels
    2. non_dimensional.nusselt(…) –
  2. solver.initial(...)